## Slide 1: Introduction to ARDUINO and Programming

## Slide 2: About Arduino Uno
Reset button
14 Digital I/O pins (6 PWM)
6 Analog Input pins
3.3 V and 5 V outputs
USB port
12 V input
http://www.farnell.com/datasheets/1682209.pdf

## Slide 3: Setting up Arduino IDE

## Slide 4: Structure of an Arduino code
1. Define Variables
2. Setting up functions
3. Eternal loop
void setup()
{}
void loop()
{}
Setup function is run once, when the microcontroller boots up or resets.
After setup function the processor moves to run code inside the loop function. Code inside loop function will be run over and over until the microcontroller is shut down.
int pin = 1;
Before going to the setup function constant variables should be defined
It’s required to have both setup() and loop() functions in the code

## Slide 5: Example 1 - Blinking led
You need
  Breadboard
  Led
  Resistor (270 ohm)
  Arduino
  Wires

## Slide 6: Example 1
http://blog.grifby.com/2013/04/tutorial-1-blinking-led-using-arduino.html

## Slide 7: Arduino C – Basic functions
pinMode(var1, var2)
pinMode functions sets the mode of given pin. Var1 is the number of the pin and var2 is the mode (INPUT, OUTPUT)
digitalWrite changes the status of the pin. Var1 is the number of the pin and var2 is the status (LOW, HIGH).
digitalWrite(var1, var2)

## Slide 8: Writing your first program
int ledPin = 13;
void setup()
{
pinMode(ledPin, OUTPUT);
}
void loop()
{
digitalWrite(ledPin, HIGH);
delay(1000);
digitalWrite(ledPin, LOW);
delay(1000);
}
Basic blinking LED

## Slide 9: Writing your first program
int ledPin = 13; //Variable to store the pin number
void setup()
{
pinMode(ledPin, OUTPUT); //set ledPin as output
}
void loop()
{
digitalWrite(ledPin, HIGH); //LED ON
delay(1000); //Wait 1000ms (=1s)
digitalWrite(ledPin, LOW); //LED OFF
delay(1000); //Wait 1000ms (=1s)
}
Basic blinking LED

## Slide 10: Uploading the program
Click Verify
  The program is checked
Click Upload
  The program is uploaded to the Arduino mCu board
1.
2.